## Slide 1: VLSI Architecture for EMT Simulation
Presented by: Rajat Sharma
Under Professor : Weiping Shi

## Slide 2: TABLE OF CONTENT (MODULES)
SERIAL NO | MODULE | SLIDES
1 | EMT Network and Problem description | 3-4
2 | Exciter (observation for filter) | 5- 8
3 | Filter (1 -2 -3) order | 9-34
4 | Limiter | 35-45

## Slide 3: EMT Network
Figure : 1 (EMT Network)

## Slide 4: Problem Description
Important part in hardware EMT simulation system is the control elements.
Control elements can be expressed in form of transfer function.
In the exciter or other control elements, multiple transfer functions are connected in series or in parallel to express the relationship between inputs and outputs.
Need to break down and categorize Transfer functions for effective system simulation.
Develop a programmable transfer function that can be configured to represent various transfer functions by adjusting the coefficients.

## Slide 5: Control Elements:

## Slide 6: Exciter (Observation)
Most of the exciter modules are basically a control block comprising of various first order transfer function.
Take a example below:
Figure 2: Exciter BPA EA - Continuously acting DC rotating excitation system model.
Variables:
VT: Magnitude of the bus terminal voltage.
VREF: Voltage reference set point, used to control the desired output voltage.
VSTB: Power system stabilizer output signal (in this case, it is set to zero).
VMAX: Upper voltage limitation to prevent over-voltage in the system.
VMIN: Lower voltage limitation to prevent under-voltage in the system.
EFD: Generator field voltage, which controls the excitation of the generator.
Constants:
TR: Time constant of the voltage transducer, determining how quickly the system reacts to changes in VT.
TA: Time constant of the amplifier, affecting the speed of amplification of the control signal.
TA1: Additional time constant for amplifier dynamics.
TE: Time constant of the exciter, influencing how fast the excitation system responds.
TF: Time constant of the field, related to the field winding of the generator.
SE: Saturation function in terms of the generator field voltage (EFD), which helps to model the non-linear behavior of the exciter.

## Slide 7: Input/Output
  The input to the Exciter system is the generator terminal voltage from the transmission line.
  The signal is passed through a Finite Impulse Response (FIR) filter to remove high-frequency noise.
  Voltage magnitude extraction is performed.
  The processed signal is fed into the exciter transfer function control block.
  The transfer function control block consists of various filter blocks arranged in series and parallel to generate the desired output signal.
  Output: The final output is the controlled excitation signal that regulates the generator’s field voltage, ensuring stable operation of the generator.

## Slide 8: Observation: Exciter filter order
  The transfer functions consist of:
        Integrator
        First-Order Lag
        Derivative
        Lead-Lag
  These transfer functions are primarily first-order.
  Implementation Approach:
        Create a general first-order transfer function block.
        Program the block’s coefficients to realize specific transfer functions.
  The transfer functions represent digital filters like:
        FIR (Finite Impulse Response)
        IIR (Infinite Impulse Response)

## Slide 9: Type of Filters
Here, in Exciter there are two types of digital filter in discrete time domain:
1) IIR filter
            is discrete time output of the filter.
            N, M is the order of the filter.
            is the gain of the filter.
            is the discrete time input to the filter.
2) FIR filter :
            is discrete time output of the filter.
            m is the order of the filter.
            is the gain of the filter.
            is the discrete time input to the filter.

## Slide 10: General:1st order transfer function
For the s, domain general 1st order transfer function.
Which is equivalent to,
        Rearranging,

## Slide 11
By applying the inverse Laplace transform to the above expression, we obtain the following differential equation:
Substituting the values for time domain,

## Slide 12: 1st order transfer function (S domain: Euler's approximation)
Figure 3: Block diagram of 1st order filter

## Slide 13: Multiplier block
Multiplier
a
b
a/ b / a *b
Figure : Multiplier Block

## Slide 14: Connector Block
A
B
A / B
C
A / C
Here, the connector block is used to connect two adder together.
A is output from the current level adder.
B is the output from the previous adder.
C is the input from the next adder.
Figure 4: Connector Block
A

## Slide 15: Arithmetic block
The arithmetic block accepts two input variables for multiplication. The multiplication result can then be added to a variable received from either:
The next connector block , if streaming data is available
A previous connector block, if streaming data is available
Multiplier block
Adder
β
X(t)
inp_from_X(t+δt)
inp_prev_multiplier_result
out_multiplier_result
inp_curr_Variable
inp_streaming_result_from_above_to_below
out_X(t)
inp_streaming_result_from_below_to_above
out_result_from_adder

## Slide 16: FPFA - logical block
Multiplier block
Adder
β
X(t)
inp_from_X(t+δt)
inp_curr_Variable
inp_prev_multiplier_result
inp_streaming_result_from_above_to_below
out_streaming_result_from_below_to_above
out_result_from_adder
out_streaming_result_from_above_to_below
inp_streaming_result_from_below_to_above
FPFA_logical_block
Short-hand representation
in_curr
in_X(t+δt)
in_p_m
in_s_a_b
out_s_b_a
out_res
out_s_a_b
in_s_b_a
out_X(t)
out_multiplier_result
out_X(t)
out_m

## Slide 17: 1st order filter implementation
Maximum delay for 2nd order implementation is 1 multiplier, 3 adder and 3 mux.
Here,
A = 𝑦(𝑡) ⋅𝛼
B =𝑥(𝑡+Δ𝑡)⋅𝛽
C = 𝑥(𝑡)⋅𝛾
F = 𝑦(𝑡+Δ𝑡) “ Feedback”

## Slide 18
Multiplier block
Adder
β
X(t+δt)
Multiplier block
Adder
γ
X(t)
Multiplier block
Adder
α
Y(t)
A
B
C
D = A + B
E = C + D
Y(t+δt) = A + B + C
Here, the Total delay for 1st order Filter from input to availability in feedback path :
MUX : 3
Adder: 2
Multiplier: 1
NOTE: BUS WIDTH IS SAME EVERY WHERE: IT IS VARIABLE FOR NOW.
Figure 5: 1st order Filter Implementation

## Slide 19
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
Symbol Multiplier output
A
B
C
A+B
Y(t+δt) = A+B+ C
1st order Filter implementation in FPFA fabric
Critical path delay = 1 multiplier + 3 Adder (approx.)

## Slide 20: General:2nd order transfer function
For the s, domain general 2nd order transfer function.
This is a second-order system, where Y(s) is the output and X(s) is the input. This can also be written as:
Converting to time domain,

## Slide 21
Using Euler's approximation,

## Slide 22: 2nd order transfer function (S domain: Euler's approximation)
Figure 6 : Block diagram of 2nd order filter

## Slide 23
2nd Order implementation of Configurable filter block
Maximum delay for 2nd order implementation is 1 multiplier, 3 adder and 3 mux.
Here,
B =𝑥(𝑡)⋅𝛼
A =𝑥(𝑡+Δ𝑡)⋅𝛽
C = 𝑥(𝑡−Δ𝑡)⋅𝛾
D = 𝑦(𝑡)⋅𝛿
E = 𝑦(𝑡−Δ𝑡)⋅𝜖
F = A + B
G = F + C
H = D + E
I = 𝑦(𝑡+Δ𝑡) = A + B + C +D + E = H + G

## Slide 24
Multiplier block
Adder
β
X(t+δt)
Multiplier block
Adder
α
X(t)
Multiplier block
Adder
γ
X(t-δt)
Multiplier block
Adder
δ
Y(t)
Multiplier block
Adder
ε
Y(t-δt)
A
B
C
D
E
F = A + B
F = A + B
G = F + C
G = F + C
H = D + E
H = D + E
I = H + G
Y(t) = A + B + C + D+ E
Here, the Total delay for 2nd order Filter from input to availability in feedback path :
MUX : 5
Adder: 3
Multiplier : 1
NOTE: BUS WIDTH IS SAME EVERY WHERE: IT IS VARIABLE FOR NOW.
Figure 7: 2nd order Filter Implementation

## Slide 25
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
Symbol Multiplier output
A
B
C
D
E
A+B
i = A+B+ C
j = D+E
Y(t+δt) = i + j
2nd order Filter implementation in FPFA fabric
Critical path delay = 3 Adder + 1 multiplier (approx.)

## Slide 26: General:3rd order transfer function
For the s, domain general 3rd order transfer function.

## Slide 27
Substituting approximation:

## Slide 28: 3rd order Implementation
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
Critical path delay =
1 Multiplier + 3 Adder (approx.)
A
B
C
D
E
F
G
H
A + B
C + D
Y = A +B+ C + D
G + H
E + F
X = E +F+ G + H
X + Y
Symbol Multiplier results
Output

## Slide 29: General:4th order transfer function
Taking inverse Laplace transform:

## Slide 30
Substituting approximation

## Slide 31: Technical Achievements
Merge Two 1st Order Filters
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
(s)

## Slide 32: Technical Achievements
Connect Two 1st Order Filters
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block

## Slide 33: Technical Achievements
BPA EA - Continuously acting DC rotating exciter model

## Slide 34
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
Limiter
Limiter
Limiter
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
BPA EA model Implementation
Delay for respective logic,
1st order filter = 1 multiplier + 2 adder
Summation = 1 adder
Limiter logic delay = Limiter delay + 1 adder
Elements in the critical path,
Total no of 1st order filter = 5
Total no of summation = 4
Limiter logic = 1
Critical path delay = 5 multiplier + 14 adder + 1 limiter delay (approx.)

## Slide 35: Alternate architecture : 2nd order capable
S0
S1
S2
S3
M
1
c
b
a
2
3
d
5
6
S4
S5
S6
S7
4
S8

## Slide 36
Multiplier
Multiplier
Multiplier
Adder
Adder
Multiplier
Multiplier
Multiplier
Adder
Adder
Adder
Limiter
Variable register bank
Constant register bank
A1
A2
A3 A2 A1
A3
Core
var<5:0> 6 Channels
(each of 16 bit fixed point no)
1st order filter
const<5:0> 6 Channels
(each of 16bit fixed point no)
1st order filter
A1
A2
A3
const<0>
Var<1>
Var<2>
Var<3>
Var<4>
Var<5>
Var<0>
const<1>
const<2>
const<3>
const<4>
const<5>

## Slide 37
X(t+δt)
Selector
(select 1 among different bank)
X(t)
y(t)
X(t)
y(t)
X(t+δt)
X(t)
y(t)
6th Filter
A3 - Pre
y(t)
X(t+δt)
X(t)
y(t)
Decoder (A3)
Decoder (A2)
Decoder (A1)
C1
C2
C3
C4
C5
C6
Selector
Constant registers banks
(Parallel - in -> parallel - out)
Variable registers banks (Parallel - in -> Parallel – out)
X(t+δt)
X(t)
y(t)
Magnitude extraction
A3
A2
A1
6 Channels
6 Channels
6 Channels
S1.reg
S2.reg
S4.reg
C1
C2
C3
C4
C5
C6
C1
C2
C3
C4
C5
C6
C1
C2
C3
C4
C5
C6
5th Filter
S3.reg
X(t)

## Slide 38
Multiplier
Multiplier
Multiplier
Adder
Adder
Variable register bank
Constant register bank
A_feedback
A_feedback
Core
var<2:0> 3 Channels
(each of 16 bit fixed point no)
1st order filter
const<2:0> 3 Channels
(each of 16bit fixed point no)
const<0>
Var<1>
Var<2>
Var<0>
const<1>
const<2>
Limiter
Limi_out

## Slide 39
X(t+δt)
Selector
(select 1 among different bank)
X(t)
y(t)
X(t+δt)
X(t)
y(t)
Decoder (A2)
Variable registers banks (Parallel - in -> Parallel – out)
A_feedback
3 Channels
S0.reg
S8.reg
X(t+δt)
X(t)
y(t)
X(t+δt)
X(t)
y(t)
S7.reg
S6.reg
Lim_out
S7(out)
HOLD
S5.reg
X(t+δt)
X(t)
y(t)
S4.reg
X(t+δt)
X(t)
y(t)
S3.reg
S1.reg
S0(out)
S1(out)
S8(out)
HOLD
S2.reg
Magnitude extraction
Limiter output (S5.reg) step

## Slide 40
C1
C2
C3
Selector
Constant registers banks
(Parallel - in -> parallel - out)
3 Channels
C1
C2
C3
C1
C2
C3
C1
C2
C3
C1
C2
C3
C1
C2
C3
C1
C2
C3
C1
C2
C3
C1
C2
C3

## Slide 41: Limiter:
Requirement: In the EMT simulator model, the output of the Regulator must be constrained between ​ and ​ to suppress unwanted noise in the signal.
Hence, we need to design a Limiter, with minimum latency.
Figure 8: Limiter in EMT simulator

## Slide 42: Limiter design 1: (RIPPLE – Limiter )
We will modify the basic ripple comparator, to compare both min and max together in same stage block.
in_gt
in_eq
in_lt
out_gt
out_eq
out_lt
Igt
Ieq
Ilt
Stage
a
b
a
b
Figure 9: The ripple carry adder provided can compare two bits.
The goal is to expand its functionality to compare a given number with specified maximum and minimum values and ensure that the number remains constrained within this range.
Figure 10 : The designed Limiter takes the maximum (max), minimum (min), and the given number as inputs. It outputs whether the given number is equal to the minimum, equal to the maximum, greater than the maximum, or less than the minimum.
Figure 9: Basic Comparator
Figure 10: Limiter stage block
Inp_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Inp_gt_max
Inp_eq_max
Inp_lt_min
a
max
a
max
min
Inp_eq_min
Inp_eq_min
out_eq_min
min

## Slide 43: RIPPLE – Limiter Equation
  out_eq_min = output bit representing that a is equal to min
  out_eq_max = output bit representing that a is equal to max
  out_gt_max = output bit representing that a is greater than max
  out_lt_min = output bit representing that a is smaller than min
  Inp_gt_max = input bit representing that a is greater than max
  Inp_eq_max = input bit representing that a is equal to max
  Inp_lt_min = input bit representing that a is smaller than min
  Inp_eq_min = input bit representing that a is equal to min
EQUATION:
out_eq_min = Inp_eq_min * ( a XNOR min)
out_eq_max = Inp_eq_max * (a XNOR max)
out_gt_max = Inp_gt_max + (Inp_eq_max * a* max’)
out_lt_min = Inp_lt_min + (Inp_eq_min * a’ * min)
Inp_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Inp_gt_max
Inp_eq_max
Inp_lt_min
Stage
a
max
a
max
min
Inp_eq_min
Inp_eq_min
out_eq_min
min
Figure 11: Limiter stage block
If out = min or out < min : y = min ;
else if out = max or out > max : y = max;
else: y = a ;

## Slide 44: Ripple Comparator: (Block Diagram)
out_eq_min
out_lt_min
out_eq_max
out_gt_max
min
max
a
Inp_lt_min
Inp_eq_min
Inp_eq_max
Inp_gt_max
Critical path delay (1 bit) = 1 Xnor + 1 and gate delay (approx.)

## Slide 45: Selector : (block diagram)
min
max
a
out_lt_min
out_eq_min
out_eq_max
out_gt_max
y
Critical path delay (1bit) = 3 or + 2 and gate delay (approx.)

## Slide 46: RIPPLE – Limiter Block diagram
This is 4 bit limiter, similarly it can be expanded to 8 bit, 16bit, 32bit etc.
a1 | b1 | out
0 | 0 | a
0 | 1 | min
1 | 0 | max
Figure 12: 4bit (min/max) comparator
Inp_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Inp_gt_max
Inp_eq_max
Inp_lt_min
Stage3
a3
max3
a
max
min3
Inp_eq_min
Inp_eq_min
out_eq_min
min
inr_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Stage2
a2
max2
a
max
min2
Inp_eq_min
out_eq_min
min
inr_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Stage1
a1
max1
a
max
min1
Inp_eq_min
out_eq_min
min
inr_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Stage0
a0
max0
a
max
min0
Inp_eq_min
out_eq_min
min
out_eq_min
out_lt_min
out_eq_max
out_gt_max
min3
a3
max3
out3
min2
a2
max2
out2
min1
a1
max1
out1
min0
a0
max0
out0
Selector
Selector
Selector
Selector
out_eq_min
out_lt_min
out_eq_max
out_gt_max
out_eq_min
out_lt_min
out_eq_max
out_gt_max
out_eq_min
out_lt_min
out_eq_max
out_gt_max

## Slide 47: Delay – Ripple limiter
4 bit = 4 * (1 xnor + 1 and) + (3 or + 2 and gate delay) = (4 xnor + 3 or + 6 and) gate delay
16 bit = 16 * (1 xnor + 1 and) + (3 or + 2 and gate delay) = (16 xnor + 3 or + 18 and) gate delay
32 bit = 32 * (1 xnor + 1 and) + (3 or + 2 and gate delay) = (32 xnor + 3 or + 34 and) gate delay

## Slide 48: Comparator based Limiter: X–OR–NOR cell based design (4 bit)
This is a design for 4 bit comparator, for finding
If a is less or equal, similar design can be made
To find if a is greater or equal.
a3 min/max_3
a2 min/max_2
a1 min/max_1
a0 min/max_0
A_LT_MIN
A_E_MIN
Here,
a = input variable (4 bit)
min = min value a variable can have
max = max value a variable can have
A_E_MIN = a is equal to min/max
A_LT_MIN = a is less then min/max
Figure 13 : XNOR based Comparator
Referenced : High-speed and area-efficient scalable N-bit
digital comparator : ISSN 1751-858X
A_E_MIN

## Slide 49
Referenced design

## Slide 50
a3 min3
a2 min2
a1 min1
a0 min0
A_LT_MIN
A_E_MIN
a3 max3
a2 max2
a1 max1
a0 max0
A_GT_MAX
A_E_MAX
4 bit - State block : Block diagram

## Slide 51: 4 bit selector
max (0-3)
a(0-3)
min(0-3)
A_LT_MIN
A_GT_MAX
A_E_MIN
A_E_MAX
out(0-3)
selector
A_LT_MIN
A_GT_MAX
A_E_MIN
A_E_MAX
out(0-3)
a (0-3)
min(0-3)
max(0-3)

## Slide 52
Stage3
a3
max3
a
max
min3
min
A_LT_MIN
A_GT_MAX
A_E_MIN
A_E_MAX
Stage2
a2
max2
a
max
min2
min
A_LT_MIN
A_GT_MAX
A_E_MIN
A_E_MAX
Stage1
a1
max1
a
max
min1
min
A_LT_MIN
A_GT_MAX
A_E_MIN
A_E_MAX
Stage0
a0
max0
a
max
min0
min
A_LT_MIN
A_GT_MAX
A_E_MIN
A_E_MAX
16 – bit (Limiter design)
selector
out(0-3)
a (0-3)
min(0-3)
max(0-3)
selector
out(4-7)
a (4-7)
min(4-7)
max(4-7)
selector
out(8-11)
a (8-11)
min(8-11)
max(8-11)
selector
out(12-15)
a (12-15)
min(12-15)
max(12-15)
16 – bit _XNOR : Limiter

## Slide 53: Delay – XNOR limiter
4 bit = (2 xnor + 2 nand + 1 or + 1 nor + 1 tristate buffer ) gate delay
16 bit = (2 xnor + 2 nand + 2 and (5 input) + 1 and (4 input) + 1 or + 1 nor + 1 tristate buffer ) gate delay
32 bit = (2 xnor + 2 nand + 6 and (5 input) + 1 and (4 input) + 1 or + 1 nor + 1 tristate buffer ) gate delay

## Slide 54: Miscellaneous
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
Limiter
Limiter
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
Limiter

## Slide 55
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block
FPFA_logical_block

## Slide 56
inr_gt_max
Inp_eq_max
Inp_lt_min
out_gt_max
out_eq_max
out_lt_min
Stage
a
max
a
max
min
Inp_eq_min
out_eq_min
min

## Slide 57: Alternate
Multiplier block
β
X(t)
adder
Multiplier block
β
X(t)
adder
Multiplier block
β
X(t)
adder
Multiplier block
β
X(t)
adder
Multiplier block
β
X(t)
adder
Multiplier block
β
X(t)
adder